## Slide 1: Tolerating Compound Threats in Critical Infrastructure Control Systems
Sahiti Bommareddy‡, Maher Khan†, Huzaifah Nadeem†, Benjamin Gilby†, Imes Chiu§, John W. van de Lindt¶, Omar Nofal∥, Mathaios Panteli††, Linton Wells II‡‡, Yair Amir‡, Amy Babay†
†University of Pittsburgh, ‡Johns Hopkins University, §Defense Logistics Agency, ¶Colorado State University, ∥Florida International University, ††University of Cyprus, ‡‡George Mason University
Notes: Hello. My name is <name> and I will be presenting our work on <title>. I’m from the university of Pittsburgh but this was an interdisciplinary collaboration with computer scientists, civil engineers, and electrical engineers from these universities and the Defense Logistics Agency

## Slide 2: What does ‘Compound Threat’ refer to?
Cyberattack in the aftermath of a natural hazard.
Prior work has covered:
  Crash Faults
  Byzantine Failures
  Not both together

## Slide 3: An emerging trend of such sophisticated attacks
During the 2021 Multi-State Information Sharing and Analysis Center annual exercises, 10 scenarios involved planning for the dual impact of a cyberattack and a natural disaster [JB21]
[JB21] “Natural disasters can set the stage for cyberattacks,” https://www.securityinfowatch.com/cybersecurity/news/21244746/natural-disasters-can-set-the-stage-for- cyberattacks, November 2021, retrieved August 16, 2024.
Notes: Government interest

## Slide 4: An emerging trend of such sophisticated attacks
After Hurricane Harvey in 2017, the U.S. Army Cyber Institute conducted a three-day drill simulating a cyberattack during a hurricane [JB21]
[JB21] “Natural disasters can set the stage for cyberattacks,” https://www.securityinfowatch.com/cybersecurity/news/21244746/natural-disasters-can-set-the-stage- for- cyberattacks, November 2021, retrieved August 16, 2024.
Notes: Government interest

## Slide 5: An emerging trend of such sophisticated attacks
Cyberattacks on hospitals are also growing, including attacks during the COVID-19 pandemic [Ghayoomi+21] [SW21]
[Ghayoomi+21] H. Ghayoomi, K. Laskey, E. Miller-Hooks, C. Hooks, and M. Tariverdi, “Assessing resilience of hospitals to cyberattack,” DIGITAL HEALTH, vol. 7, 2021. [Online]. Available: https://doi.org/10.1177/20552076211059366
[SW21] “The growing threat of ransomware attacks on hospitals,” https://www.aamc.org/news-insights/growing-threat-ransomware-attacks-hospitals, July 2021, retrieved August 16, 2024.
Notes: Government interest

## Slide 6: Motivation
Natural hazards are a problem
Existing works only tackle cyberattacks, and not compound threats
Power grids are extremely important for other critical infrastructure systems
An emerging trend of sophisticated cyberattacks on damaged infrastructure
Notes: On existing works: as we’ll see compound threats presents more challenges than just plain cyberattacks and just natural hazards (just crashes).

## Slide 7: Goal
Analyze system design implications of compound threats for power grid SCADA systems

## Slide 8: Outcome
Our work shows that compound threats remain a challenging problem with no complete solution
BUT
  Explicitly considering natural hazards in system design can improve resilience (next few slides)
  Reconfiguration can help (will get to this later)

## Slide 9: Contributions
Compound threat model
Compound-Threat Analyzer
Case studies for sites in Hawaii and Florida
No existing SCADA architectures (including state of the art architectures) adequately addresses the compound threat problem (next)
Reconfiguration can help (will get to this later)
  Reconfiguration capability in Spire [Babay+18]
[Babay+18] A. Babay, T. Tantillo, T. Aron, M. Platania, and Y. Amir, “Network-attack-resilient intrusion-tolerant SCADA for the power grid,” in
IEEE/IFIP International Conference on Dependable Systems and Networks (DSN), June 2018, pp. 255–266.
Notes: 4. == Our work shows that compound threats remain a challenging problem with no complete solution

## Slide 10: System and Threat Model

## Slide 11: Supervisory Control and Data Acquisition (SCADA)
SCADA systems provide power grids with monitoring and control capabilities
Components:
  Human Machine Interface (HMI)
  SCADA Master (SM)
  Programmable Logic Controllers (PLCs) and Remote Terminal Units (RTUs)
Conventional SCADA system architecture
(reproduced from [Babay+19])
[Babay+19] A. Babay, J. Schultz, T. Tantillo, S. Beckley, E. Jordan, K. Ruddell, K. Jordan, and Y. Amir, “Deploying intrusion-tolerant SCADA for the
power grid,” in 49th Annual IEEE/IFIP International Conference on Dependable Systems and Networks (DSN), Portland, Oregon, June 2019

## Slide 12: SCADA Architectures
Current Industry-Standard SCADA Architectures [Babay+18]
Configuration “2”
Configuration “2-2”
[Babay+18] A. Babay, T. Tantillo, T. Aron, M. Platania, and Y. Amir, “Network-attack-resilient intrusion-tolerant SCADA for the power grid,” in
IEEE/IFIP International Conference on Dependable Systems and Networks (DSN), June 2018, pp. 255–266.
Notes: This is Fig 1 (a) = left and (b) = right in the paper.
Left can tolerate one SM CRASH only. Right can tolerate one SM crash AND primary site unavailability (with manual intervention – delay in the order of minutes)
These are NOT Intrusion tolerant and NEITHER Network attack resilient

## Slide 13: SCADA Architectures
Intrusion Tolerant Architectures [Babay+18]
  Byzantine fault tolerant replication
Configuration “6”
Configuration “6-6”
[Babay+18] A. Babay, T. Tantillo, T. Aron, M. Platania, and Y. Amir, “Network-attack-resilient intrusion-tolerant SCADA for the power grid,” in
IEEE/IFIP International Conference on Dependable Systems and Networks (DSN), June 2018, pp. 255–266.
Notes: This is Fig 3 (a) = left and (b) = right in the paper.

## Slide 14: SCADA Architectures
Network-Attack-Resilient Intrusion-Tolerant Architecture [Babay+18]
Configuration “6+6+6”
[Babay+18] A. Babay, T. Tantillo, T. Aron, M. Platania, and Y. Amir, “Network-attack-resilient intrusion-tolerant SCADA for the power grid,” in
IEEE/IFIP International Conference on Dependable Systems and Networks (DSN), June 2018, pp. 255–266.
Notes: MENTION DATA CENTER
This is Fig 4 (a) = left and (b) = right in the paper.
Simultaneous one intrusion + one site isolation

## Slide 15: Sites and Configurations
Hawaii
  Honolulu + Waiau + DRFortress
    Honolulu: already used
    Waiau: central location + good connectivity
      + under consideration in future
    DRFortress: commercial data center
  Hurricanes: 5 hurricanes simulated
    Hurricane paths used by emergency planners
    Hurricane realizations using a wave-surge model based on ADvanced CIRCulation model [LWS92]
[LWS92] R. A. Luettich, J. J. Westerink, and N. W. Scheffner, “ADCIRC: an advanced three-dimensional circulation model for shelves, coasts, and
estuaries. report 1, theory and methodology of ADCIRC-2DD1 and ADCIRC-3DL,” Dredging Research Program, U.S. Army Engineers
Waterways Experiment Station, Vicksburg, MS, Tech. Rep. DRP-92-6, 1992.
Notes: around 10 min ok until here
This is Fig 5 in the paper.

## Slide 16: Sites and Configurations
Florida
  Palm Beach + Port Orange + Jacksonville Tierpoint
    Palm Beach: currently used & invested in
    Port Orange: currently used as backup (public info.)
    Jacksonville Tierpoint: commercial data center
  Hurricanes: No hurricane paths but a worst-case scenario
    not feasible to simulate hurricane impacts at the scale of the whole site
    100-year flood hazard intensity for each site
    Basically, the level of flooding that has a 1% chance of being reached or exceeded each year
    Based on NOAA’s and FEMA’s models
Notes: This is Fig 6.
Reason for HI FL difference: Detailed flooding data not available for FL (due to large size of the state)
NOAA = National Oceanic and Atmospheric Administration
FEMA = Federal Emergency Management Agency

## Slide 17: System operational states outcomes
Colored states from Spire [Babay+18]
  Green: all good
  Red: system not operational but safe
  Orange: non-operational until back up restored
  Gray: compromise
[Babay+18] A. Babay, T. Tantillo, T. Aron, M. Platania, and Y. Amir, “Network-attack-resilient intrusion-tolerant SCADA for the power grid,” in
IEEE/IFIP International Conference on Dependable Systems and Networks (DSN), June 2018, pp. 255–266.
Notes: Explain what safe means

## Slide 18: Threat Scenarios & Attack Models
Threat scenarios:
  Natural Hazard
  Natural Hazard + Server intrusion
  Natural Hazard + Site isolation (e.g. by DDOS)
  Natural Hazard + Server intrusion + Site isolation
Attack Models
  Worst case
    Deterministic
    gray > red > orange > green
  Uniformly Random

## Slide 19: Results
Notes: 15 min mark

## Slide 20: Worst-case (Hawaii)
Hurricane only (No Cyberattack)
  Control Center 1 (CC1): Honolulu
  Control Center 2 (CC2): Waiau
  Data Center (DC) : DRFortress
CC1 and CC2 go down together in 9.5% of the instances. DC remains safe
CC1, CC2, and the DC survive the hurricane
DC alone cannot keep the system running

## Slide 21: Worst-case (Hawaii)
Hurricane + Server Intrusion
Control Center 1 (CC1): Honolulu
Control Center 2 (CC2): Waiau
Data Center (DC) : DRFortress
When CC1 survives the hurricane, the intrusion takes us to the compromised state (gray)
The intrusion is not a problem the intrusion tolerant architectures
(otherwise, same as previous slide)
The hurricane takes the CCs down before the attacker gets a chance to attack
Notes: only need to explain red for 2 and 2-2 (other ones repeat prev slide)

## Slide 22: Worst-case (Hawaii)
Hurricane + Site Isolation
Control Center 1 (CC1): Honolulu
Control Center 2 (CC2): Waiau
Data Center (DC) : DRFortress
There is only one site (CC1). So even when it survives the hurricane, site isolation takes us to the red state (not operational but safe)
Where we have two sites, when they survive the hurricane (90.5% of the instances), because of the site isolation, we need to manually move to the back up (delay)
This architecture can tolerate 1 Site Isolation (CC1 and CC2 survive the hurricane in 90.5% of instances).
When all of our sites are down (due to either the hurricane ( in 2-2, and 6-6) and both the hurricane + the attack (6+6+6)
Notes: previewing what to expect with random is probably too much to explain here

## Slide 23: Worst-case (Hawaii)
Hurricane + Server Intrusion + Site Isolation
The two non intrusion-tolerant architectures are in the compromised state when the CCs survive the hurricane.
When the CCs do not survive the hurricane, we get the non-operational state since the attacker have nothing to attack. Reminder: for Hawaii, both CCs go down together.
Control Center 1 (CC1): Honolulu
Control Center 2 (CC2): Waiau
Data Center (DC) : DRFortress
Same as before.
(These are intrusion tolerant configurations)

## Slide 24: Worst-case (Florida)
Control Center 1 (CC1): Palm Beach
Control Center 2 (CC2): Port Orange
Data Center (DC) : Jacksonville Tierpoint
100% ‘all good’ (green) state even with the hurricane?
FPL invested in a Category-5-hurricane-resilient control center at Palm Beach. So, the investment pays off!
We still have cyberattacks (intrusions) to worry about in these two configurations
We are good here because of the hurricane-resistant CC1 and the intrusion tolerant configurations
Notes: FPL = Florida Power & Light

## Slide 25: Worst-case (Florida)
Control Center 1 (CC1): Palm Beach
Control Center 2 (CC2): Port Orange
Data Center (DC) : Jacksonville Tierpoint
Even though CC1 survives the hurricane, the attacker isolates it. We can move to the back up in 2-2 and 6-6 (with delay) IF it survived the hurricane (58.5%).
6+6+6 can still function when CC2 survives the hurricane (and CC1 is isolated).
Unlike Hawaii, we do not get any red state for these. Since CC1 (Palm Beach) always survives the hurricane, the intrusion will get us.
These are intrusion tolerant. Other than that, same logic follows as in just Hurricane + Site Isolation scenario.
Notes: FPL = Florida Power & Light

## Slide 26: Takeaways from Worst-case results
Only configuration “6+6+6” is able to tolerate both server intrusion and site isolation attacks: it maintains a green operational state as long as the control centers survive the hurricane
Hurricane-resilient sites (such as Palm Beach) can help with the hurricane
  But, this is not enough to withstand compound threats involving site isolation attacks

## Slide 27: Random (Hawaii)
Hurricane + Server Intrusion + Site Isolation
Worst-Case Attack Model
(for comparison)
Uniformly Random Attack Model
In the random model, the attacker can target the back up CC. We are still in the green state in that situation.
Notes: For HI: with WC, 6-6 was 90.5% orange. Now that orange is divided into orange and green. Rest all same
Conclusion: random provides a diff view. Essentially a range WC-Random. Single sites not good at all. Diffs in two sited. Three sited not much diff.

## Slide 28: Random (Florida)
Hurricane + Server Intrusion + Site Isolation
In worst-case, the attacker always attacked the primary CC.
In random, it can be either one.
Worst-Case Attack Model
(for comparison)
Uniformly Random Attack Model
Notes: For FL: with WC, in 2-2 red and green. In 6-6 diff percentages and 3 colors now (in WC it was red + orange). 6+6+6 diff percentages same colors

## Slide 29: Random (Florida)
Hurricane + Server Intrusion + Site Isolation
Worst-Case Attack Model
(for comparison)
Uniformly Random Attack Model
Similar to Hawaii, the attacker can attack the back up.
But, the percentage of red is different?
Notes: For FL: with WC, in 2-2 red and green. In 6-6 diff percentages and 3 colors now (in WC it was red + orange). 6+6+6 diff percentages same colors

## Slide 30: Random (Florida)
Hurricane + Server Intrusion + Site Isolation
Worst-Case Attack Model
(for comparison)
Uniformly Random Attack Model
The values are different. In Hawaii, the two CCs went down together. In Florida, that is not always the case.
Notes: For FL: with WC, in 2-2 red and green. In 6-6 diff percentages and 3 colors now (in WC it was red + orange). 6+6+6 diff percentages same colors

## Slide 31: Random (Florida)
Hurricane + Server Intrusion + Site Isolation
Worst-Case Attack Model
(for comparison)
Uniformly Random Attack Model
We get worse results (with regards to the red state) for 6+6+6 as compared to 6-6?
For “6+6+6”, when Port Orange (CC2) is flooded, the attacker can isolate
either Palm Beach or the data center at Jacksonville
Notes: For FL: with WC, in 2-2 red and green. In 6-6 diff percentages and 3 colors now (in WC it was red + orange). 6+6+6 diff percentages same colors

## Slide 32: Takeaways from Random results
An important drawback of the generally more resilient configuration “6+6+6”:
  It can become non-operational even when one control center remains fully correct and available
Random attack model results show that the inability of existing architectures to withstand compound threats is not an artifact of the strong worst-case selection model
  Even under this weaker model, no architecture achieves a fully available (green) operational profile

## Slide 33: Alternative Sites
Worst-Case
(Hurricane + Server Intrusion)
Uniformly Random
(Hurricane + Site Isolation)
Honolulu and Waiau always went down together.
But Honolulu and Kahe never go down at the same time
Control Center 1 (CC1): Honolulu
Control Center 2 (CC2): Waiau / Kahe
Data Center (DC) : DRFortress
With Kahe as our CC2, when Honolulu goes down, Kahe and DRFortress can keep the system fully available
If the attacker can isolate any site, we are better with the choice of Kahe, but still not completely resilient
Notes: Currently, Waiau is planned as a backup because it is a location with strong network connectivity and resources. But due to geographical profile, it may not be the best choice
“slightly confusing to compare different threat models; make this clear in explanation”

## Slide 34: Takeaways from Alt. Sites results
It is possible to improve resilience by explicitly considering the natural hazard in designing the system
However, even when natural hazard impacts are used to guide the control center selection, there is still no architecture that completely withstands the full compound threat model

## Slide 35: Reconfiguration
An example for Florida:
However, when we have one of the CCs available, we can reconfigure to a “6” configuration
Normally 6+6+6 is better than 6-6
But when one of the CCs and DC become unavailable, we get worse results.
And get strictly better results than 6-6
We chose Jacksonville for our DC, but Miami was an equally good choice (from a geographical perspective)
Worst-Case Analysis:
Server Intrusion + Site Isolation
Notes: Miami was equally as good as Jacksonville from a geographical perspective so we picked Jack.. But we could have gone for miami too

## Slide 36: Reconfiguration
With Random Model
  Server Intrusion + Site Isolation
It is also possible to reconfigure
preemptively to exclude the data center in situations where it makes us more vulnerable e.g. when the DC is already unavailable, or when a CC is flooded or isolated.
Notes: Further new: preemptive

## Slide 37: Takeaways from Reconfig. results
Reconfiguration can help us resume operation in some situations
If there is time to reconfigure the system after losing one site but before losing the other, then preemptive reconfiguration avoids the temporary interruption (orange state), converting it to green.
  Thus, with the addition of reconfiguration, “6+6+6” becomes strictly better than “6-6”.

## Slide 38: Conclusion
Our work shows that compound threats remain a challenging problem with no complete solution
BUT
  Explicitly considering natural hazards in system design can improve resilience
    e.g. for Hawaii, Kahe is a better choice over Waiau
  Reconfiguration can help
    e.g. with the addition of reconfiguration, “6+6+6” becomes strictly better than “6-6”

## Slide 39: Questions? h.nadeem@pitt.edu
Compound-Threat Analyzer can be found at:
https://github.com/spire-resilient-systems/compound_threat_analyzer

## Slide 40: Alternative Sites
Data Center for Florida:
Notes: Alt sites for CC2

## Slide 41: Out-of-Band vs. In-band reconfiguration
Why manual OOB reconfiguration?
  Attackers may try to exploit use the automatic reconfiguration mechanism e.g. use repeated reconfiguration requests as a DOS attack, or to reconfigure to replicas they control.
  For in band, need a quorum of up and correct replicas to reconfigure

## Slide 43: Tolerating Compound Threats in Critical Infrastructure Control Systems
Sahiti Bommareddy‡, Maher Khan†, Huzaifah Nadeem†, Benjamin Gilby†, Imes Chiu§, John W. van de Lindt¶, Omar Nofal∥, Mathaios Panteli††, Linton Wells II‡‡, Yair Amir‡, Amy Babay†
†University of Pittsburgh, ‡Johns Hopkins University, §Defense Logistics Agency, ¶Colorado State University, ∥Florida International University, ††University of Cyprus, ‡‡George Mason University
Notes: I’m from the university of Pittsburgh but this was a collaborative work with these universities and the DLA. It was an interdisciplinary collaboration with from computer scientists, civil engineers, electrical engineers .

## Slide 44: What does ‘Compound Threat’ refer to?
Cyberattack in the aftermath of a natural hazard.
Prior work has covered:
  Ex. 1: One site flooded
  Ex. 2: One site attacked
  Ex. 3: Both
✓
✓
✓
: ✓
: ✗
: ✓

## Slide 45
Analysis tool: